## Slide 1
Sea ice buoys at AWI
Activity Report 2015
IABP Meeting
Seattle, Washington
8-10 June 2015
Mario Hoppmann, Marcel Nicolaus, Benjamin Rabe & colleagues

## Slide 2: SAMS IMB operation times
Energy budgets
Antarctic
Arctic
Green: alive
Black: dead
Notes: More own deployments in ARC & ANT

## Slide 3: Snow Buoy operation times
Energy budgets
Antarctic
Arctic
Green: alive
Black: dead
Photo: A. Mahoney (U Alaska)
Notes: More own deployments in ARC & ANT

## Slide 4: Progress
Snow buoy reliability increased
  Stability of mast and wiring, Controller upgrade, Static discharge, sonic sensor upgrade
24 deployments, 12 still active, longest record ~ 850 days
20 ordered/in transit
Additional developments
  Data processing routine completed
  Manuscript planned
  Online portal (aim: common data base for all units)
Deployment sheets
Data into Global Telecommunication System (GTS)

## Slide 5: Radiation Buoy
3 spectral radiometer (TriOS)
Incoming, reflected, transmitted irradiance
Campbell logger & iridium transmission
Lead batteries & solar panel
Deployment of improved unit in Sept 2015

## Slide 6: Active deployments
Cooperation Ch. Haas, HH, MPI, FMI, NPI, …
Cooperation P. Heil, FMI, BAS ..

## Slide 7: New infrastructure project: FRAM
Energy budgets
Infrastructure program: „Frontiers in Arctic Marine Monitoring“
2015-2019
Develop/maintain Arctic observation network
Money for all sorts of stuff (Lander, AUV, Glider, ROV, Buoys, Remote sensing,…)
Data Portal
„Automonous platforms“ work package
(Mario Hoppmann, Marcel Nicolaus, Benjamin Rabe, Frank Wenzhöfer)
Antarctic covered by other funding
Notes: More own deployments in ARC & ANT

## Slide 8
FRAM WP „Automonous platforms“
Main task:
Establish & maintain network
of autonomous, ice-based (multi-disciplinary) platforms in the Transpolar Drift
Observations of sea ice, atmosphere and upper ocean
Multi-disciplinary approach: combination of physical, biological and biogeochemical observations at same spot

## Slide 9
WHOI
Metocean
Multi-disciplinary approach
Atmosphere
Sea ice & snow
Upper Ocean
Air temperature
Surface temperature
Barometric pressure
Relative Humidity
Wind speed & -direction
Radiation
Surface albedo
Snow depth
Sea-ice mass balance (growth & melt)
Light transmission
Temperature, Salinity,
Current velocity,
Dissolved Oxygen
Chl-a, CDOM, PAR, POC,
Nitrate, ph

## Slide 10: Drifting bio-physical observatory
CAFF. 2010. Arctic Biodiversity Trends: Selected indicators of change

## Slide 11: Buoy Developments within FRAM
Energy budgets
Maintain IMB, SVP, Snow Buoy, ITP deployments
Sensor comparisons/data quality assessment: PS
Bio-profiling platforms: WHOI, MetOcean
(Chl-a, CDOM, backscatter, PAR, Oxygen, Nitrate, ph)
Bio-optical buoy (non-profiling)
ADCP buoy
Camera buoy
Optimize data flow
Data portal
Notes: More own deployments in ARC & ANT

## Slide 12: Antarctic Plans 2015/16 (PS96)
  9 Snow buoys (AWI)
  9 SAMS IMBs (AWI)
  10 SVP (AWI & AAD)
  2 Bio-Phys (AWI)
  Additions ?
Cape Town
8 Dec 2015
Punta Arenas
6 Feb 2016
Similar to 2013/14

## Slide 13
Transarc2 (2015)
Contrasts (2017)
WHOI
L‘OCEAN
Metocean
+ Icearc2 (2018), Transarc3 (2019)
Arctic Plans (Polarstern)

## Slide 14: Arctic Plans 2015
PS94 “TransArc II”
Follow-up to 2011’s “Transarc”
16 Aug 2015 (Tromsø) -
15 Oct 2015 (BHV)
8 Snow Buoys
8 SAMS IMBs
8 SVPs
1 PAWS (weather station)
1 Radiation station
2 Bio-ITPs
6 IAOOS (France)

## Slide 15: Arctic Plans 2016+2017
Polarstern PS101
15 Oct 2016 – 21 Nov 2016
Gakkelridge
Testing of prototypes
(Bio-ITP, Camera, ADCP,…)
“Contrasts” (Marcel)
MYI/FYI/thin ice comparison north of Greenland
Deployment of multi-disciplinary arrays
Number of buoys similar to 2015
Approval pending

## Slide 16: Buoy-related PhD projects & internships
Freshwater distribution in the Arctic / North Atlantic: Myriel Horn, supervised by Benjamin Rabe & Co
Buoy/remote sensing comparison, SAMS IMB data processing, spatio-temporal variability/how many buoys needed..
?, supervised by Marcel Nicolaus
3. Interns & students for
ADCP buoy /snow buoy /SAMS IMB data processing, database

## Slide 17: Data Portal and Archive
http://www.meereisportal.de
http://www.seaiceportal.de

## Slide 18: Data Portal and Archive
http://www.meereisportal.de
http://www.seaiceportal.de
English version available soon
Buoy tracks (daily maps)
Buoy data, links to PANGAEA
Sensor characterization (in progress)
Deployment information
  Snow buoy and IMB collection
  (cooperations: FMI Bin Cheng, MPI Met. HH Kaleschke, MPI Bremen Wenzhöfer
Others welcome (no AWI site!), support included
Need Input!

## Slide 19: Discussion points
What we need:
Input related to data portal, external partners
Opinions which new developments are needed most
Our list: camera buoy, ADCP & current meter buoy,
bio-CTD-profiler, under-ice near-surface bio
Collaborations on such developments
More affordable buoys, e.g. AWS
Probably deployment opportunities
A better way to manage iridium transmission
What we can offer:
Logistics & Infrastructure as usual
Data portal & support for specific buoy types (not AWI-only!)
Remote sensing data (lots of efforts currently at AWI)
Financial resources
Lots of interested scientists!